## Slide 1: Memory Persistency
Steven Pelley, Peter M. Chen, Thomas F. Wenisch

## Slide 2: Nonvolatile memory (NVRAM)
Low latency random access, durable
NVRAM enables persistent main memory
Storage technology | Random read latency | Durable?
Disk | 10ms | 
Flash | 90µs | 
DRAM | 100ns | 
NVRAM | 50-1000ns [IBM] | 

## Slide 3: NVRAM recovery
Writes unordered!
writes
Must constrain write order for recovery
Cache eviction reorders writes to memory
Enforcing program order writes incurs 30x slowdown over instruction execution rate.
Must constrain writes for correctness, but reorder for performance

## Slide 4: Memory order
Writes to memory reorder
But loads/stores between processors and cores ordered: memory consistency

Use memory consistency to reason about NVRAM write order
?

## Slide 5: Memory persistency
Build on memory consistency, providing models to constrain NVRAM write order
Relax persistency to improve write concurrency, increasing throughput
This project: focus on models (interface), rather than implementations

## Slide 6: Outline
Define memory persistency
Persistent queue benchmark
Memory persistency models
Methodology
Evaluation

## Slide 7: Recovery observer
Memory consistency:
Constrain order of loads and Stores Between processors
Memory persistency:
Imagine failure as recovery observer
Atomically copies persistent address space to NVRAM at failure, adhering to consistency model
Real memory systems must provide appearance of this model
Enforcing persist order equivalent to enforcing store order

## Slide 8: Strict persistency
Couples consistency and persistency
  1:1 mapping between observable volatile and persistent states
Any two stores that may only be observed in some order implies ordered persists
  The store and the persist are the same event
Use consistency model and memory barriers to constrain persist order
  as well as thread synchronization

## Slide 9: Strict persistency/SC
Sequential consistency (SC), enforcing same order for persists and stores
Persists from each thread must not be observed out of program order after failure
Persists from different threads must be observed as interleaving of program orders

## Slide 10: Strict persistency/RMO
Relaxed Memory Order (RMO), coupling thread synchronization and persists
Barriers constrain memory operation order (and thus persist order)
Persists on single thread now concurrent

## Slide 11: Buffered persistency
Thread execution (volatile state) proceeds ahead of persistent state
  Recovery observer lags arbitrarily behind
Problem: side effects violate model
Persist sync forces durable state to “catch up”
…
Persist to object A
PersistSync
Syscall() // network
…
May observe syscall but after recovery fail to see persist to A
PersistSync constrains order

## Slide 12: Relaxed persistency
Decouple thread synchronization and persists
  Persist order may deviate from store order
  Store and persist are separate events
Additional persist barriers order persists
Later I’ll introduce relaxed persistency models assuming SC as underlying consistency model

## Slide 13: Relaxed persistency example
Lock()
Persist 0x100
Persist 0x108
…
Persist flag=1
Unlock()
Lock provides thread synchronization. No need to additionally enforce persist order at this point
flag must not persist before data, but as the lock protects against data races an additional memory barrier is unnecessary
Memory barrier
Persist barrier
Memory barrier
Precise, independent control over consistency and persistency
Simultaneously relaxed consistency and persistency gets complicated.
Stores reorder around persist barriers, persist reorder around store barriers

## Slide 14: Memory Persistency Design Space
Persistency
Consistency
Sequential consistency (SC), persistent state must match volatile state
Loads, stores, and persists may all reorder. Minimizes delays for persists and thread synchronization
SC, but persistent state de-coupled from volatile states. Persists may reorder
Relaxed consistency, persistent state matches volatile state
Persist order determined by new persist barriers
Persist order determined by consistency model
strict
relaxed

## Slide 15: Outline
Define Memory Persistency
Persistency models
Evaluation

## Slide 16: Persistent Queue
Useful as log/journal in file systems and db
Features:
  Serialize inserts
  Recovered queue disallows or detects holes
Goal: maximize volatile performance (instruction execution rate) and improve persist concurrency for inserts
Implementation: based on circular buffer
  Data segment, head marks next location to insert

## Slide 17: Queue Designs
Copy-while-locked (CWL)
  Single lock protects insert operation
Two-Lock Concurrent
  Different locks to reserve and update head
  Lesson: thread concurrency creates persist concurrency even for strict persistency
Queue-holes [IBM]
  Detect holes. Single lock but concurrent copies
Focus on CWL (see dissertation for others)

## Slide 18: Copy-While-Locked Queue
Insert(entry, length):
lock(queue_lock)
data[head] = length
data[head+sizeof(length)] = entry
head += length + sizeof(length)
unlock(queue_lock)
Data
Head
Persistency model must enforce persist orderings
Persist Ordering Constraints

## Slide 19: Persistency assumptions and goals
Assume all persists occur in-place (no logging)
Assume persist buffering
  Thread state proceeds ahead of persists
  But persists still occur in proper order
  Persist order critical path limits performance
Assume persist coalescing
  Persists to the same address may coalesce (persist only last value) if no ordering constraints violated
Goal: create models to minimize critical path

## Slide 20: New persistency models
All models use SC as consistency model
  Easier to reason about (removes relaxed consistency/relaxed persistency weirdness)
  Easier to evaluate (memory tracing observes SC)
Successively relax persistency to improve persist concurrency/reduce critical path

## Slide 21: Model 1: strict persistency
Any volatile memory state that might be observed by the recovery observer processor under SC is an allowable persistent state
Equivalent: two stores guaranteed to be ordered w.r.t. recovery observer implies ordered persists
Persist sync allows ordering persists with visible side effects (syscall)

## Slide 22: Strict persistency queue
Persist order determined by program order
Insert(entry, length):
lock(queue_lock)
data[head] = length
data[head+sizeof(length)] = entry
head += length + sizeof(length)
unlock(queue_lock)
Lock serializes persists between threads
Large entries persist in program order
No code annotation necessary!

## Slide 23: Strict persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2
Minimal dependences shown. Persists to head likely to coalesce

## Slide 24: Strict persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2
Guarantees correct recovery, but over-constraints persists

## Slide 25: Strict persistency implementations
Delay execution at each persist
Serialize persists when reserving memory bus
Queue persists from each thread, detecting access races (including synchronization races) that introduce order across threads
Combine HTM and hardware durable transactions
  Persistent bulkSC?

## Slide 26: Model 2: epoch persistency
Motivation: persisting large objects with SC introduces program-order constraints.
Instead, use persist barrier to divide execution into persist epochs.
Persists within each epoch are concurrent
Data sharing continues to observer SC
Determining persist order between threads can get tricky

## Slide 27: Persist epoch races (PER)
Under what circumstances are persists between threads ordered?
Persist epoch race: 2+ threads contain epochs that race (including sync. races) and at least one epoch persists
Thread 1
Barrier
Persist A
Persist B
Barrier
Thread 2
Barrier
Read B
Persist A’
Barrier
Can A’ persist before A?
Can A’ persist before B?
Epochs aren’t serializable!

## Slide 28: Epoch persistency queue, 1st attempt
Insert(entry, length):
barrier()
lock(queue_lock)
barrier()
data[head] = length
data[head+sizeof(length)] = entry
barrier()
head += length + sizeof(length)
barrier()
unlock(queue_lock)
barrier()
Surround lock/unlock with barriers to prevent PER. Serializes inserts
Barrier ensures head does
not persist before data, but data persists concurrently

## Slide 29: Race-free epoch persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2

## Slide 30: Race-free epoch persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2

## Slide 31: Race-free epoch persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2
Entries persist in parallel, but inserts still serialized

## Slide 32: Epoch persistency ordering with PER
Persist A ordered before persist B if:
  Race (sync or data) in epoch after A and in epoch prior to B (same rule as in absence of PER)
  Or A and B are to the same address (even if epochs race)
Otherwise concurrent

## Slide 33: PER persist ordering
Thread 1: A | B C
Thread 2: C’ D | E
A before E (race and barriers)
C before C’ (cache coherence)
A before C’ (transitivity)
C before E (transitivity)
PersistPersist race good candidate for coalescing
PersistPersist
Thread 1: A | B C
Thread 2: load C D | E
A before E (race and barriers)
Not C before E
PersistLoad
Thread 1: A | B load C
Thread 2: C D | E
A before E (race and barriers)
LoadPersist
Thread 1: A | B C
Thread 2: C D | E
A before E (race and barriers)
C is volatile
PER orders persists outside of racing epochs, except for cache coherence

## Slide 34: Epoch persistency queue, 2nd attempt
Insert(entry, length):
barrier()
lock(queue_lock)
barrier()
data[head] = length
data[head+sizeof(length)] = entry
barrier()
head += length + sizeof(length)
barrier()
unlock(queue_lock)
barrier()
Allow persist epoch races
head persists ordered by cache coherence

## Slide 35: Epoch persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2

## Slide 36: Epoch persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2

## Slide 37: Epoch persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2
Entries on different threads persist in parallel

## Slide 38: Epoch persistency implementation
Similar to BPFS (see paper/dissertation)
Queue persists from each thread, record persist barriers, only enforce order at barriers
Persistent BulkSC (transactions)
  Use persist barrier knowledge to optimize persistent transactions and intelligently place transaction boundaries

## Slide 39: Model 3: strand persistency
Motivation: epochs only allow adjacent persists on same thread or persists in racing epochs to be labeled concurrent
Divide execution into strands
  NewStrand begins a strand
  Strands execute in order on a thread, but from perspective of persistency are independent.
  Equiv: a new strand clears persist dependences
  Races/conflicts introduce order between strands
Epoch pers. orders persists within strands

## Slide 40: Strand examples
Strands allow precise persist constraint labeling
A
B
C
...
Epoch
A
Barrier
B
C
A
B
Barrier
C
B must be ordered with either A or C
or
Strand
NewStrand
A
Barrier
C
NewStrand
B
...

## Slide 41: Perfect constraint labeling
For each persist:
  New strand
  Read all addresses persist depends on
  Barrier
  Persist
Creates DAG of dependences. Edge from each read to persist
Minimal persist dependences (introduces additional instructions)

## Slide 42: Strand persistency queue
Insert(entry, length):
lock(queue_lock)
new_strand()
data[head] = length
data[head+sizeof(length)] = entry
barrier()
head += length + sizeof(length)
unlock(queue_lock)
Removes unnecessary dependences between inserts

## Slide 43: Strand persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2

## Slide 44: Strand persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2

## Slide 45: Strand persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2
Back to minimal dependences

## Slide 46: Outline
Define Memory Persistency
Persistency models
Evaluation

## Slide 47: Methodology
Assume buffered NVRAM with infinite banks (no conflicts ever occur). All persists occur in place (no logging but persists may coalesce)
Either
  Persists drain faster than instruction execution rate; instructions limit performance
  Persists drain slower than instruction execution rate; persist rate limits performance
Determine slower of the two and resulting throughput

## Slide 48: Methodology
Measure execution rate on real server
  2.4 GHz Xeon E5645
  Use 1 and 8 threads to test concurrency
  Pad to 64 bytes to remove false sharing
  Repeatedly insert 100-byte entries as quickly as possible, reporting insert rate

## Slide 49: Methodology
Measure persist rate via memory traces
  Produce SC memory trace from PIN
  Annotate barriers, persistent malloc, etc.
Persist critical path from simulation
  Track persist dependences at variable granularity
  Persists coalesce assuming variable atomic persist
  (both 8 bytes by default)
  Observe persist timing and dependences from persistency model

## Slide 50: Relaxed persistency
Relaxed persistency removes constraints and regains throughput
Line indicates instruction execution rate
Assumes 500ns persists
30x
Other queues

## Slide 51: Persist latency
Relaxed persistency tolerates greater persist latency
17ns
119ns
6.2µs
1 Thread
(8 Threads)

## Slide 52: Persist coalescing
Larger atomic persists improve concurrency for strict models

## Slide 53: Persistent false sharing
Coarse dependence tracking reintroduces constraints

## Slide 54: Conclusion
Must order persists, but over-constraining hurts performance (resembles consistency)
Memory persistency builds on consistency to enforce persist order
Persistency may be relaxed, de-coupling store and persist order constraints
Relaxed persistency enables instruction execution rate with recovery correctness

## Slide 55: Thank You!
Thanks to my family, friends, Tom, committee, collaborators, and all of you

## Slide 56: Backup Slides
Persistency definition
  Defining order of persists to same address
Queue
  Circular buffer
  Other queue designs
Results
  Coalescing
  Relaxed persistency, all queues
  Effect of latency on CWL, 8 threads
Related work
  BPFS

## Slide 57: Persists to same address
Strict persistency relies on consistency model to define order or persists to same address
  Often relies on cache coherence guarantees
Relaxed consistency/relaxed persistency allows:
  Store visibility to reorder across persist barrier
  Persists to reorder across store barrier
May violate cache coherence persist ordering

## Slide 58: Persists to same address
Thread 1’s stores reorder around the barrier
Persist ordering dependences shown for barriers and cache coherence order
Dependence cycle cannot be enforced
Thread 1:
Persist A
Barrier
Persist B
Thread 2:
Persist B
Barrier
Persist A

## Slide 59: Persists to same address
Resolve by:
  Relying on strict persistency
  Preventing stores from reordering around persist barriers
  Defining additional synchronization to prevent such situations
    Interaction between consistency barriers and persist barriers
Back
Backup slides

## Slide 60: Coalescing
Any two persists may coalesce if:
  Hardware allows them to persist atomically
  No happens-before constraints are violated
Given a DAG of persist constraints, coalescing:
  Combines the two persists into a single node
  Node takes union of edges into and out of node
  Edges entirely inside the node go away
  Coalescing legal if no cycles introduced

## Slide 61: Coalescing example
A
B
A’
B
A/A’
Cycle!
C
D
C’
A
B
E
A
B
C/C’
D
E

Back -- Backup slides

## Slide 62: All queues, 1 thread
Varied volatile performance. Require strand persistency

## Slide 63: All queues, 8 threads
Multi-threading improves persist concurrency. Epochs sufficient
Back -- Backup slides

## Slide 64: Latency, CWL 8 threads
Epoch persistency likely sufficient
28ns
1.6µs
10.5µs
PER-free: 202ns (not shown)
Back -- Backup slides

## Slide 65: BPFS
“Better IO Through Byte-Addressable, Persistent Memory”
Cache implementation of barriers and epochs
  Stalls to persist at thread conflicts
  Flush cache for persist sync
Differences
  Programmer must provide isolated epochs (including false sharing, otherwise deadlock)
  No dependences through volatile memory
  Introduces dependences according to TSO
Back Backup slides

## Slide 66: [dependence template]
Data
Head
Data
Head
Thread 1
Thread 2