## Slide 1: Database and System Design for Emerging Storage Technologies
Steven Pelley
Committee:
Thomas F. Wenisch (Chair)
Michael J. Caffarella
Peter M. Chen
Zhengya Zhang

## Slide 2: Future storage technologies
Flash no longer scaling
  Need high capacity, low energy persistent storage
DRAM no longer scaling
  Need high performance volatile storage
New nonvolatile memories (NVRAM) might provide both!
  Phase change (PCM)
  Memristor (from HP)
  Spin-transfer torque (STT RAM)

## Slide 3: Nonvolatile memory (NVRAM)
Low latency random access, durable
NVRAM enables persistent main memory
Storage technology | Random read latency | Durable?
Disk | 10ms | 
Flash | 90µs | 
DRAM | 100ns | 
NVRAM | 50-1000ns [IBM] | 

## Slide 4: Accelerating recoverable systems
NVRAM reduces storage access delays
  Redesign software at a high level assuming low-cost accesses
Leverage native memory instruction interface to remove additional software overheads
  Reduce memory copy operations
  Improve concurrency/synchronization
NVRAM removes delays and stalls due to storage access

## Slide 5: Example: transaction processing (VLDB)
As disk replacement NVRAM enables near-instant recovery
Disk-management overheads impose bottleneck
~ 30 15krpm disks
or 3 Flash SSDs
[device IOPS rates: Symantec]

## Slide 6: Ensuring correct recovery
Constrain order of persistent writes
Current memory systems allow memory writes to reorder
  Cache eviction order ≠ store order
Require persist barriers
  File system/disk sync()
  Many possible implementations
Despite fast NVRAM accesses, persist barriers limit performance

## Slide 7: NVRAM group commit
Time
Undo log
Updates
Couple transaction and durability management
Amortize persist barrier cost over many transactions
Minimal software overhead/complexity
Transactions quiesce at end of batch
Transaction updates write atomically using batch log

## Slide 8: Recovery management performance
Group commit helps, but high performance barriers ideal

## Slide 9: Practical persist barriers
How do we minimize barrier stalls?
How do barriers behave with shared memory?
How poor is performance if we simply enforce program order of NVRAM writes?
explore fundamental primitives for persist synchronization

## Slide 10: Memory ordering
Writes to memory reorder
But loads/stores between processors and cores ordered: memory consistency

Extend memory consistency to reason about NVRAM write order: Memory Persistency
?

## Slide 11: Thesis
Using Flash memory for analytics
  ADMS 2011
Using NVRAM to accelerate transactions
  Upcoming VLDB
Memory persistency (focus of this talk)
  Extend memory consistency to reason about the order of NVRAM writes
  Program order NVRAM writes limit throughput to 1/30th instruction execution rate
  New persistency models regain performance

## Slide 12: Outline
Motivate memory persistency
Memory consistency review
Define memory persistency
Persistent queue benchmark
Memory persistency models
Methodology
Evaluation

## Slide 13: Memory consistency primer
Motivation: reorder instructions while providing intended shared memory behavior
Store barrier
Thread 2:
If (Flag == 1) {
localBuffer[0] ← Buffer[0]
localBuffer[8] ← Buffer[8]
…
}
In isolation may reorder, but when sharing must constraint
Thread 1:
Buffer[0] ← 1
Buffer[8] ← 1
…
Flag ← 1
Load barrier

## Slide 14: Memory consistency models
Consistency spectrum
Guarantees for reasoning about reordering
Sequential Consistency (SC): no reordering, memory appears as a switch
Relaxed Memory Order (RMO): complete reordering, must use barriers
Model separate from implementation

## Slide 15: Recovery observer
Memory consistency:
Constrain order of loads and stores between processors
Memory persistency:
Imagine failure as recovery observer
Atomically copies to NVRAM at failure, adhering to consistency model
Treats failure as a processor
Enforcing NVRAM write order equivalent to enforcing store order

## Slide 16: Strict persistency
Couples consistency and persistency
  1:1 mapping between observable volatile and persistent states
Any two stores that may only be observed in some order implies ordered persists
  The store and the persist are the same event
Consistency model and barriers constrain persist order and thread synchronization
Implementation free to optimize

## Slide 17: Strict persistency/SC
SC, enforcing order for persists and stores
Persists from each thread must not be observed out of program order after failure
Persists from different threads must be observed as interleaving of program orders
  Volatile accesses may order persists!

## Slide 18: Buffered persistency
Thread execution (volatile state) proceeds ahead of persistent state
  Recovery observer lags arbitrarily behind
Problem: side effects violate model
Persist sync forces durable state to “catch up”
…
Persist to object A
PersistSync
Syscall() // network
…
May observe syscall but after recovery fail to see persist to A
PersistSync constrains order

## Slide 19: Strict persistency/RMO
Barriers constrain memory operation order
  Barriers that order stores also order persists
Persists on single thread now concurrent
Barriers enforce both persist and store visibility order, even when only one required

## Slide 20: Relaxed persistency
Decouple thread synchronization and persists
  Store and persist are separate events
  Persist order may deviate from store order
New persist barriers order persists
Allows thread to observe persist values without introducing order dependence
Later I’ll introduce relaxed persistency models assuming SC as underlying consistency model

## Slide 21: Relaxed persistency example
Lock()
Persist 0x100
Persist 0x108
…
Persist flag=1
Unlock()
Lock provides thread synchronization. No need to additionally enforce persist order at this point
flag must not persist before data, but as the lock protects against data races an additional memory barrier is unnecessary
Memory barrier
Persist barrier
Memory barrier
Precise, independent control over consistency and persistency
Stores reorder around persist barriers, persists reorder around store barriers.
Simultaneously relaxed consistency and persistency gets complicated.

## Slide 22: Memory Persistency Design Space
Persistency
Consistency
Sequential consistency (SC), persistent state must match volatile state
Loads, stores, and persists may all reorder. Minimizes delays for persists and thread synchronization
SC, but persistent state de-coupled from volatile states. Persists may reorder
Relaxed consistency, persistent state matches volatile state
Persist order determined by new persist barriers
Persist order determined by consistency model
strict
relaxed

## Slide 23: Outline
Define Memory Persistency
Persistency models
Evaluation

## Slide 24: Persistent Queue
Useful as log/journal in file systems and db
Features:
  Serialize inserts
  Recovered queue disallows or detects holes
Goal: maximize volatile performance (instruction execution rate) and improve persist concurrency for inserts
Implementation: based on circular buffer
  head marks next location to insert

## Slide 25: Queue Designs
Copy-while-locked (CWL)
  Single lock protects insert operation
Two-Lock Concurrent
  Different locks to reserve and update head
  Lesson: thread concurrency creates persist concurrency even for strict persistency
Queue-holes [IBM]
  Detect holes. Single lock but concurrent copies
Focus on CWL (see dissertation for others)

## Slide 26: Copy-While-Locked Queue
Insert(entry, length):
lock(queue_lock)
data[head] = length
data[head+sizeof(length)] = entry
head += length + sizeof(length)
unlock(queue_lock)
Data
Head
Persistency model must enforce persist orderings
Persist Ordering Constraints

## Slide 27: Persistency assumptions and goals
Assume all persists occur in-place (no logging)
  Persist ordering constraint implies delay
Assume persist buffering
  Persist critical path limits persist rate
Assume limited atomic persists and coalescing
  E.g., 8-byte atomic persists
  Persists to the same address may coalesce (persist only last value) if no ordering constraints violated
Goal: create models to minimize persist critical path

## Slide 28: New persistency models
All models use SC as consistency model
  Easier to reason about (removes relaxed consistency/relaxed persistency weirdness)
  Easier to evaluate (memory tracing observes SC)
Successively relax persistency to improve persist concurrency/reduce critical path

## Slide 29: Model 1: strict persistency
Any volatile memory state that might be observed by the recovery observer processor under SC is an allowable persistent state
Equivalent: two stores ordered w.r.t. recovery observer implies ordered persists
  Same thread: program order
  Different threads: synchronization
Persist sync allows ordering persists with visible side effects (syscall)

## Slide 30: Strict persistency queue
Persist order determined by program order
Insert(entry, length):
lock(queue_lock)
data[head] = length
data[head+sizeof(length)] = entry
head += length + sizeof(length)
unlock(queue_lock)
Lock serializes persists between threads
Large entries persist in program order
No code annotation necessary!

## Slide 31: Strict persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2
Minimal dependences shown. Persists to head likely to coalesce

## Slide 32: Strict persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2
Guarantees correct recovery, but over-constrains persists

## Slide 33: Strict persistency implementations
Delay execution at each persist
Serialize persists when reserving memory bus
Queue persists from each thread, detecting access races (including synchronization races) that introduce order across threads
Combine HTM and hardware durable transactions
  Persistent bulkSC?

## Slide 34: Model 2: epoch persistency
Motivation: persisting large objects with SC introduces program-order constraints.
Instead, use persist barrier to divide execution into persist epochs, ordering persists
Data sharing continues to observe SC
Persist order resembles RMO, persist barrier acts as a full memory barrier

## Slide 35: Persist epoch races (PER)
Under what circumstances are persists between threads ordered?
Persist epoch race: 2+ threads contain epochs that race (including sync. races) and at least one epoch persists
Thread 1
Barrier
Persist A
Persist B
Barrier
Thread 2
Barrier
Read B
Persist A’
Barrier
Can A’ persist before A?
Can A’ persist before B?
Epochs aren’t serializable!

## Slide 36: Epoch persistency queue, 1st attempt
Insert(entry, length):
barrier()
lock(queue_lock)
barrier()
data[head] = length
data[head+sizeof(length)] = entry
barrier()
head += length + sizeof(length)
barrier()
unlock(queue_lock)
barrier()
Surround lock/unlock with barriers to prevent PER. Serializes inserts
Barrier ensures head does
not persist before data, but data persists concurrently

## Slide 37: Race-free epoch persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2

## Slide 38: Race-free epoch persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2

## Slide 39: Race-free epoch persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2
Entries persist in parallel, but inserts still serialized

## Slide 40: Relaxed persist ordering
Memory operations (including volatile) have a persistent memory order
  This order contains fewer partial order constraints than SC execution
Rule 1: memory operations from same thread separated by persist barrier are ordered
Rule 2: operations that conflict (same address, at least 1 write) ordered by SC execution
  What to call this? Not a race because they aren’t adjacent in any SC execution
Resembles RMO persist order (but SC synchronization and values)

## Slide 41: Another way to say this
Assume only specific partial orders from SC
Rule 1: partial orders within each thread that cross a persist barrier
Rule 2: partial orders within and across threads due to accesses to the same address where at least one access is a store/persist
For strand persistency rule 1 becomes: partial orders within each strand that cross a persist barrier

## Slide 42: Persist ordering example
Rule 1: A before {B, C}; E before F; G before H
Rule 2: C before E; F before G
Trans.: A before {E ,F, G, H}; E before {G, H}
B concurrent with {C, E, F, G, H} (even though value of operations may depend on B)
Dependences propagate regardless of operation type (load, store, persist) including volatile operations
Thread 1: A | B C
Thread 2: E | F
Thread 3: G | H
conflict

## Slide 43: Epoch persistency queue, 2nd attempt
Insert(entry, length):
barrier()
lock(queue_lock)
barrier()
data[head] = length
data[head+sizeof(length)] = entry
barrier()
head += length + sizeof(length)
barrier()
unlock(queue_lock)
barrier()
Allow persist epoch races
head persists from different inserts ordered due to conflicts

## Slide 44: Epoch persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2

## Slide 45: Epoch persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2

## Slide 46: Epoch persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2
Entries on different threads persist in parallel

## Slide 47: Epoch persistency implementation
Similar to BPFS (see paper/dissertation)
Queue persists from each thread, record persist barriers, only enforce order at barriers
Persistent BulkSC (transactions)
  Use persist barrier knowledge to optimize persistent transactions and intelligently place transaction boundaries

## Slide 48: Model 3: strand persistency
Motivation: epochs allow limited concurrency
Divide execution into strands
  NewStrand begins a strand
  Strands execute in order on threads, but from persistency standpoint are independent threads
  Equiv: a new strand clears persist dependences
  Races/conflicts introduce order between strands
Epoch pers. orders persists within strands

## Slide 49: Strand persistency ordering
Rule 1: memory operations from same strand separated by persist barrier are ordered
Rule 2: operations that conflict (same address, at least 1 write) ordered by SC execution
  Such conflicts consider each strand as a separate thread (operations on same thread may conflict)
  Strand order within a thread determines order of conflicts

## Slide 50: Strand examples
Strands allow precise persist constraint labeling
A
B
C
...
Epoch
A
Barrier
B
C
A
B
Barrier
C
B must be ordered with either A or C
or
Strand
NewStrand
A
Barrier
C
NewStrand
B
...

## Slide 51: Perfect constraint labeling
For each persist:
  New strand
  Read all addresses persist depends on
  Barrier
  Persist
Creates DAG of dependences. Edge from each read to persist
Minimal persist dependences (introduces additional instructions)

## Slide 52: Strand persistency queue
Insert(entry, length):
lock(queue_lock)
new_strand()
data[head] = length
data[head+sizeof(length)] = entry
barrier()
head += length + sizeof(length)
unlock(queue_lock)
Removes unnecessary dependences between inserts

## Slide 53: Strand persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2

## Slide 54: Strand persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2

## Slide 55: Strand persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2
Back to minimal dependences

## Slide 56: Outline
Define Memory Persistency
Persistency models
Evaluation

## Slide 57: Methodology
Assume buffered NVRAM with infinite banks (no conflicts ever occur). All persists occur in place (no logging but persists may coalesce)
Either
  Persists drain faster than instruction execution rate; instructions limit performance
  Persists drain slower than instruction execution rate; persist rate limits performance
Determine slower of the two and resulting throughput

## Slide 58: Methodology
Measure execution rate on real server
  2.4 GHz Xeon E5645
  Use 1 and 8 threads to test concurrency
  Pad to 64 bytes to remove false sharing
  Repeatedly insert 100-byte entries as quickly as possible, reporting insert rate

## Slide 59: Methodology
Measure persist rate via memory traces
  Produce SC memory trace from PIN
  Annotate barriers, persistent malloc, etc.
Persist critical path from simulation
  Track persist dependences at variable granularity
  Persists coalesce assuming variable atomic persist
  (both 8 bytes by default)
  Observe persist timing and dependences from persistency model

## Slide 60: Relaxed persistency
Relaxed persistency removes constraints and regains throughput
Line indicates instruction execution rate
Assumes 500ns persists
30x
Other queues

## Slide 61: Persist latency
Relaxed persistency tolerates greater persist latency
17ns
119ns
6.2µs
1 Thread
(8 Threads)

## Slide 62: Persist coalescing
Larger atomic persists improve concurrency for strict models

## Slide 63: Persistent false sharing
Coarse dependence tracking reintroduces constraints

## Slide 64: Conclusion
Must order persists, but over-constraining hurts performance (resembles consistency)
Memory persistency builds on consistency to enforce persist order
Persistency may be relaxed, de-coupling store and persist order constraints
Relaxed persistency enables instruction execution rate with recovery correctness

## Slide 65: Thank You!
Thanks to my family, friends, Tom, committee, collaborators, and all of you

## Slide 66: Backup Slides
Persistency definition
  Defining order of persists to same address
Queue
  Circular buffer
  Other queue designs
Results
  Coalescing
  Relaxed persistency, all queues
  Effect of latency on CWL, 8 threads
Alternative interfaces
  Disk/block
    Moneta
  Transactions
    Various [Mnemosyne, RIO Vista, STM]
    Kiln-decouple thread synchronization from persistency control
  Barriers
    BPFS

## Slide 67: Persists to same address
Strict persistency relies on consistency model to define order or persists to same address
  Often relies on cache coherence guarantees
Relaxed consistency/relaxed persistency allows:
  Store visibility to reorder across persist barrier
  Persists to reorder across store barrier
May violate cache coherence persist ordering

## Slide 68: Persists to same address
Thread 1’s stores reorder around the barrier
Persist ordering dependences shown for barriers and cache coherence order
Dependence cycle cannot be enforced
Thread 1:
Persist A
Barrier
Persist B
Thread 2:
Persist B
Barrier
Persist A

## Slide 69: Persists to same address
Resolve by:
  Relying on strict persistency
  Preventing stores from reordering around persist barriers
  Defining additional synchronization to prevent such situations
    Interaction between consistency barriers and persist barriers
Back
Backup slides

## Slide 70: Coalescing
Any two persists may coalesce if:
  Hardware allows them to persist atomically
  No happens-before constraints are violated
Given a DAG of persist constraints, coalescing:
  Combines the two persists into a single node
  Node takes union of edges into and out of node
  Edges entirely inside the node go away
  Coalescing legal if no cycles introduced

## Slide 71: Coalescing example
A
B
A’
B
A/A’
Cycle!
C
D
C’
A
B
E
A
B
C/C’
D
E

Back -- Backup slides

## Slide 72: All queues, 1 thread
Varied volatile performance. Require strand persistency

## Slide 73: All queues, 8 threads
Multi-threading improves persist concurrency. Epochs sufficient
Back -- Backup slides

## Slide 74: Latency, CWL 8 threads
Epoch persistency likely sufficient
28ns
1.6µs
10.5µs
PER-free: 202ns (not shown)
Back -- Backup slides

## Slide 75: BPFS
“Better IO Through Byte-Addressable, Persistent Memory”
Cache implementation of barriers and epochs
  Stalls to persist at thread conflicts
  Flush cache for persist sync
Differences
  Programmer must provide isolated epochs (including false sharing, otherwise deadlock)
  No dependences through volatile memory
  Loads may bypass store in persist order (persist barrier is 3/4 RMO barrier)
Back Backup slides

## Slide 76: [dependence template]
Data
Head
Data
Head
Thread 1
Thread 2

## Slide 77: PER persist ordering
Thread 1: A | B C
Thread 2: C’ D | E
A before E (race and barriers)
C before C’ (cache coherence)
A before C’ (transitivity)
C before E (transitivity)
PersistPersist race good candidate for coalescing
PersistPersist
Thread 1: A | B C
Thread 2: load C’ D | E
C before E
A before E (transitivity; A before C)
PersistLoad
Thread 1: A | B load C
Thread 2: C’ D | E
load C before E
A before E (transitivity)
A before C’
LoadPersist
PER orders persists outside of racing epochs, except for cache coherence
Thread 1: A | B
Thread 2: B’ | C
Thread 3: C’ | D
A before D (race and barriers)
Red barrier required
B, C volatile

## Slide 78: Memory Persistency
Steven Pelley, Peter M. Chen, Thomas F. Wenisch

## Slide 79: Nonvolatile memory (NVRAM)
Low latency random access, durable
NVRAM enables persistent main memory
Storage technology | Random read latency | Durable?
Disk | 10ms | 
Flash | 90µs | 
DRAM | 100ns | 
NVRAM | 50-1000ns [IBM] | 

## Slide 80: NVRAM recovery
Writes unordered!
writes
Must constrain write order for recovery
Cache eviction reorders writes to memory
Enforcing program order writes incurs 30x slowdown over instruction execution rate.
Must constrain writes for correctness, but reorder for performance