## Slide 1: Database and System Design for Emerging Storage Technologies
Steven Pelley
Thesis Proposal

## Slide 2: Emerging storage technologies
Flash memory
Nonvolatile Memory (NVRAM)
  Phase Change (PCRAM)
  Memristor (HP)
  Spin-Torque Transfer (STT-RAM)
Devices offer immediate performance increase over disk
Storage technology | Random read latency
Disk | 10ms
Flash | 90µs
NVRAM | 50-1000ns [IBM]

## Slide 3: Optimizing systems for Flash/NVRAM
Decades of research/engineering to avoid random access on disk
Redesign/optimize database applications for most relevant storage technology
Analytics (DSS) on Flash
Transaction Processing (OLTP) on NVRAM
Ongoing: Persistent Memory Consistency
  Intuitive mechanisms to enable high persist throughput and enforce proper recovery

## Slide 4: Taking advantage of SSDs
Data should “prefer” disk or Flash
Flash accelerates random access to tables
Measure disk/Flash performance to determine
When optimal query plan shifts [ADMS ’11]
Table 1: Accessed Sequentially
Table 2: Accessed Randomly
Coarse-grain access limits ability to leverage fast random reads
Notes: Keeping this performance difference in mind, I came up with an idea.
Data may prefer either disk or flash
For example… scans
But the real contribution is that the optimal query plan, and thus performance, will depend on where the data resides.
So I needed to figure out exactly how query optimizers dealt with flash SSDs
Fix the colors in the table boxes

## Slide 5: Leveraging NVRAM for recovery
Hypothesis: Databases designed for disk limit performance with NVRAM
  Disk optimizations impose unnecessary overheads
NVRAM presents own set of obstacles
  Persist barriers to ensure proper recovery introduce delays
  Greater-than-DRAM read latency lengthens read stalls
I provide NVRAM evaluation methodology and new recovery mechanisms [VLDB submission]
New designs improve throughput and recovery

## Slide 6: Ongoing: persistent programming
Hypothesis: Recovery/durability changes instruction ordering requirements
  Writing NVRAM in program order yields poor performance
  Annotating persist order difficult and error prone
Similar to memory consistency models
  Define order that writes observed
  Persistence defines order that persists observed
Persistent Memory Consistency (PMC)
Provide high performance, intuitive persistence model

## Slide 7: Data center infrastructure (appendix)
Understanding and Abstracting Total Data Center Power [WEED ‘09]
  Data center power model encompassing all components
PowerRouting: Dynamic Power Provisioning in the DataCenter [ASPLOS ‘10]
  Better utilize installed power infrastructure by introducing power feed switching mechanisms and intelligent control
?

## Slide 8: Outline
Flash analytics – leveraging fast random reads
NVRAM OLTP recovery management
Persistent Memory Consistency (PMC)
Ex: data structure and consistency models

## Slide 9: Outline
Flash analytics – leveraging fast random reads
NVRAM OLTP recovery management
Persistent Memory Consistency (PMC)
Ex: data structure and consistency models

## Slide 10: Is Flash just a fast disk?
Selectivity (%)
Runtime (time)
Relation scan
Index scan
Flash favors random data access
relative to disk.
Ex: Scans that return < 10% of
table should use index, > 10%
scan entire table.
[Ramakrishnan and Gehrke]
Expect to shift right with Flash
Measure performance of scans and joins on disk/Flash
Determine when query plans change between devices

## Slide 11: Actual performance
Break-even points at lower selectivity than expected
Break-even points shift for only 0.9% selectivities
Disk
Flash
10% rule appropriate for pages
Notes: Distinguish between previous index line and the rowid-sort scan
Scans start with cold data

## Slide 12: Flash Implications
See proposal for join analysis and details
Flash already provides speedup over disk
Little opportunity to take advantage of device-dependent query optimization
  Large access granularity interferes with Flash’s low random read latency
Future NVRAMs provide fine-grained access
  NVRAM holds promise for recovery management

## Slide 13: Outline
Flash analytics – leveraging fast random reads
NVRAM OLTP recovery management
Persistent Memory Consistency (PMC)
Ex: data structure and consistency models

## Slide 14: Outline
Flash analytics – leveraging fast random reads
NVRAM OLTP recovery management
Persistent Memory Consistency (PMC)
Ex: data structure and consistency models

## Slide 15: NVRAM characteristics
Byte addressable reads and persistent writes
  Greater-than-DRAM read latency
  Asymmetric writes/reads (slower writes)
  MLC slows both reads and writes further
Possible interfaces – implies varied latency
  Disk replacement
  PCIe attached
  Main memory bus
Slower than DRAM, but much faster than disk/Flash

## Slide 16: Accelerating transaction processing
Online Transaction Processing (OLTP) relies on durability for recovery management
  Recovery management optimized for disk [ARIES]
Faster storage provides low latency recovery and greater transaction throughput
Define persist: write to NVRAM durably
Main-memory DB performance, disk DB recovery

## Slide 17: NVRAM OLTP opportunity
As disk replacement NVRAM enables near-instant recovery
Disk-management overheads impose bottleneck
~ 30 15krpm disks
or 3 Flash SSDs
[device IOPS rates: Symantec]

## Slide 18: Storage Management for the NVRAM Era
Methodology to evaluate NVRAM on real hardware
Implement and compare recovery management
  NVRAM Disk-Replacement has software overhead
  Persisting to NVRAM immediately as In-Place Updates, enforcing persist order with persist barriers incurs frequent synchronization delays
  Introduce new NVRAM Group Commit to minimize persist barrier frequency while trading off transaction latency
NVRAM Read performance analysis (see proposal)

## Slide 19: Background: ARIES recovery
redo
undo
redo
undo
redo
undo
Log
Store
Log orders actions from concurrent transactions Redo entries record how to repeat action
Undo entries record how to remove action
xct 1
xct 2
xct 1
Log transforms random writes into sequential writes

## Slide 20: Background: ARIES recovery
redo
undo
redo
undo
redo
undo
Log
Store
Defer page write back – may only write back after log persists
xct 1
xct 2
xct 1
Transactions commit/abort must persist before responding to client
commit
xct 2
Transactions only stall on disk write at commit

## Slide 21: Background: ARIES recovery
redo
undo
redo
undo
redo
undo
Log
Store
xct 1
xct 2
xct 1
commit
xct 2
Log is sufficient to maintain durable consistent state
On failure:
Replay log to reproduce state at the time of failure
Apply undo to remove any in-flight transactions

## Slide 22: ARIES performance overheads
redo
undo
redo
undo
redo
undo
Log
Store
xct 1
xct 2
xct 1
commit
xct 2
Optimizations necessary for disk now get in the way
Serialized log introduces large code paths and high contention
Frequent page flushing creates contention on hot page latches
Page and log flusher threads use CPU time

## Slide 23: In-Place Updates
Persist updates in place immediately
Requires persist barriers, causing transaction to stall
Requires per-update log to make page updates atomic
Always at “replayed” state
No redo, no replay
redo
undo
redo
undo
redo
undo
Log
xct 1
xct 2
xct 1
commit
xct 2
Store
Remove centralized log Undo now transaction-local
Remove centralized log, but transactions incur persist delays

## Slide 24: Choosing recovery mechanism
NVRAM Disk-Replacement incurs persist delays on page and flusher threads
  Transaction threads delay only at commit
In-Place Updates delays at each update
As persist barrier delay increases NVRAM Disk-Replacement eventually wins
Want to remove logging and synchronous persist overheads
NVRAM Group Commit – Entire batch commits or aborts

## Slide 25: NVRAM Group Commit
Time
volatile
buffer
Transactions operate on copy of data in volatile buffer
NVRAM
store
NVRAM
log

## Slide 26: NVRAM Group Commit
Time
volatile
buffer
Transactions quiesce at end of batch
NVRAM
store
NVRAM
log

## Slide 27: NVRAM Group Commit
Time
volatile
buffer
NVRAM
store
NVRAM
log
Overwritten data copied to NVRAM log
Undo log

## Slide 28: NVRAM Group Commit
Time
volatile
buffer
NVRAM
store
NVRAM
log
Undo log
Persist store
Persist batch updates in-place
Barriers ensure store persists after log

## Slide 29: NVRAM Group Commit
Time
volatile
buffer
NVRAM
store
NVRAM
log
Undo log
Persist store
Remove log
Commit transactions
Begin new batch

## Slide 30: NVRAM Group Commit
Time
volatile
buffer
NVRAM
store
NVRAM
log
Undo log
Persist store
Recovery copies valid log back to store

## Slide 31: NVRAM Group Commit
Time
Undo log
Persist store
Constant number of persist barriers per batch
No centralized logging
Throughput high so long as batch quiesce/persist short
Additional details in proposal

## Slide 32: Modeling unavailable devices
Run database on real hardware
  Log and Stores on RAMDisk
  Introduce precise delays (20ns precision using x86 RDTSCP) to model persist barrier latency
  Model persist bandwidth constraints with shared variable reservation
Build recovery mechanisms in Shore
  Rely on dirty bit fields to track buffer pool writes during transaction, page latch, or batch

## Slide 33: Recovery management performance
Group commit necessary above 2µs but increases xct latency

## Slide 34: Transaction latency
Batching increases throughput with less-than-disk latencies
3µs persist barrier latency
Normalized to 0µs in-place updates

## Slide 35: Future work
Detailed description of Group Commit and quantitative demonstration of performance
  Data structures and concurrency management
Methodology
  Quantitative validation of timing model
Evaluation
  Device lifetime and persist bandwidth constraints

## Slide 36: Summary
OLTP not yet optimized for NVRAM
Methodology to evaluate unavailable devices
Recovery mechanisms to avoid software overheads and persist synchronization delays
Consider implications of increased read latency and caching solutions (in proposal)
Efficient barriers enable simple, high performance recovery management

## Slide 37: Outline
Flash analytics – leveraging fast random reads
NVRAM OLTP recovery management
Persistent Memory Consistency (PMC)
Ex: data structure and consistency models

## Slide 38: Outline
Flash analytics – leveraging fast random reads
NVRAM OLTP recovery management
Persistent Memory Consistency (PMC)
Ex: data structure and consistency models

## Slide 39: Persistent Programming
More than databases: recoverable data structures in NVRAM
Need intuitive mechanisms to establish NVRAM persist order
  DRAM – cannot control write order
  Disk – flush cache lines and sync. Unintuitive
  Perform persists in program order – terrible performance! Must persist out of order
Persist ordering resembles memory consistency
Notes: On one extreme we might assume that things persist in program order – no additional annotation required. On the other extreme we borrow the disk interface and flush individual cache lines (much harder to program for and unintuitive).

## Slide 40: Memory consistency
Prefer to reorder instruction execution
  Complicates multi-threaded applications
Thread 1:
flag1 = 1
if flag2 == 0:
# critical sec.
Thread 2:
flag2 = 1
if flag1 == 0:
# critical sec.
flag1, flag2 initialized to 0
(Dekker’s mutex without atomic RMW)

## Slide 41: Memory consistency
Prefer to reorder instruction execution
  Complicates multi-threaded applications
Thread 1:
flag1 = 1
barrier
if flag2 == 0:
# critical sec.
Thread 2:
flag2 = 1
barrier
if flag1 == 0:
# critical sec.
Improving performance requires user intervention
CPU might reorder
flag1, flag2 initialized to 0
(Dekker’s mutex without atomic RMW)

## Slide 42: Persistent consistency
Concurrency control similar to persistence
  Consistency: order in which stores are visible
  Persistence: order in which persists are visible
Persist order must be enforced across threads
  Leverage consistency to determine persist order
Persistent Memory Consistency (PMC)
Motivate PMC, don’t consider precise implementations

## Slide 43: Outline
Flash analytics – leveraging fast random reads
NVRAM OLTP recovery management
Persistent Memory Consistency (PMC)
Ex: data structure and consistency models

## Slide 44: Outline
Flash analytics – leveraging fast random reads
NVRAM OLTP recovery management
Persistent Memory Consistency (PMC)
Ex: data structure and consistency models

## Slide 45: Persistent log/buffer
Persistent array
Persistent counter marks valid end of array
On recovery: base through counter considered valid
Buffer
array
0
1
2
3
Counter = 1
Insert(obj, size):
lock()
start = &array[counter]
memcpy(start,obj,size)
counter += size
unlock()
Buffer data must persist before counter for correct recovery

## Slide 46: Implications of persist order
Important optimization: execution runs ahead of persistent state via buffering
  Persists still occur in consistent order
If average persist throughput less than average execution rate, buffers fill
Persist order constraints limit persist parallelism and throughput
Maximize performance by minimizing persist-order critical path

## Slide 47: Persistent Sequential Consistency (PSC)
Strict
  Persists occur strictly in program order, as valid interleaving of persists between threads
  Persistent state tied to execution state
    Running instruction implies previous persists complete
    No barriers (ordering or sync) necessary
Buffered
  Persistent state lags execution state
  Requires sync barrier for external communication

## Slide 48: PSC persist constraints
Buffer atomic segment
Counter
Persists before
Insert(obj, size):
lock()
start = &array[counter]
memcpy(start,obj,size)
counter += size
unlock()
100 byte entries
8 byte atomic persist
100ns persist
Can insert every 1.4 µs (slow)
Strict consistency requires no barriers but limits performance

## Slide 49: Local Persist Order (LPO)
Remove unnecessary cross-thread ordering
Single threaded operation resembles PSC
Enforcing order across threads: 1st thread inserts persist-before, 2nd thread persist-after
  Data sharing implies persist order
  Similar to release-acquire consistency model

## Slide 50: LPO persist constraints
Single-thread constraint
Allows buffer data from multiple threads to persist concurrently
Insert(obj, size):
lock()
start = &array[counter]
memcpy(start,obj,size)
persist_after # counter persists after last
counter += size
persist_before # counter persists before next
unlock()

## Slide 51: Ideal persist constraints
Buffer persists before associated counter
Counters persist in-order
Critical path: one barrier per insert

## Slide 52: Example implementation optimization
Skip persists to counter values
Requires all counter dependencies satisfied
Critical path: bounded constant

## Slide 53: Possible directions
Evaluation
  Assume naïve implementation, measure persist critical path of simple data structures
  Is persist the bottleneck for each model?
Data structures
  Buffer
  OLTP/Shore-MT
  Batching (from OLTP design)
New consistency models when necessary

## Slide 54: Backup slides

## Slide 55: Flash memory
New durable storage popularized
by mobile devices
State stored in floating gate
Variable charge stored in
gate allows Multi-Level
Cells (MLC)
Limited write endurance
Image: Wikipedia
Flash now popular for high performance enterprise storage

## Slide 56: Flash memory performance
 | Disk | Flash
Model | WD 10Krpm | OCZ RevoDrive
Seq. Read | 120MB/s | 190MB/s
Random Read | 10ms | 90µs
$/GB | .55 | 2.5
Flash much lower read latency than disk
Flash eliminates performance difference between random and sequential accesses
Current DBMS optimized for disk
2011 devices
Notes: The sequential bandwidth is similar across devices, but random read is much faster on flash SSDs. Could possibly simplify DBMSs, which have long been optimized for high latency disks.
Say a bit more on this slide

## Slide 57: SSD query plans unchanged
Flash gives better performance, but…
Query plans do not need to be changed on Flash
  Using commercial DBMS – IBM DB2
  0.9% of scan selectivities change access path
  Join choice matters on disk, but not on Flash
Intelligent layout does not depend on query opt.
Notes: Flash is best, but found that it wasn’t better for a set of queries
Performance difference that appears on disk disappears on flash
Mention commercial systems. Not sure where
Spend more time here.

## Slide 58: Experimental structure
Focus on two key aspects of query plans
  Access paths (scan type)
  Join type
Force specific query plans and measure actual performance
Determine performance difference between devices

## Slide 59: Methodology
IBM DB2 v9.7
Intel core 2 (dual core)
2GB memory
Disk: WD VelociRaptor 10Krpm drive
Flash: OCZ RevoDrive PCIe
Wisconsin Benchmark schema and data
Notes: Limited Scope, but the simplicity of these experiments yields tremendous insight

## Slide 60: Background: DB2 access paths
Table

## Slide 61: Background: DB2 access paths
Relation scan: high selectivity
Table

## Slide 62: Background: DB2 access paths
…
Table
B-Tree index

## Slide 63: Background: DB2 access paths
…
Index scan: low selectivity
Table
B-Tree index

## Slide 64: Background: DB2 access paths
…
Table
B-Tree index

## Slide 65: Background: DB2 access paths
…
Rowids
Table
B-Tree index
{5;10}
{17;7}
{10;1}
{17;5}
Notes: Add some addresses/numbers to the rowids (2 parts, page and tuple)

## Slide 66: Background: DB2 access paths
…
Rowids
Rowid-sort scan: mid selectivities
Table
B-Tree index

## Slide 67: Background: Selecting access path
Below 10% selectivity use index scan
Above 10% selectivity use relation scan
Selectivity (%)
Runtime (time)
Relation scan
Index scan
Flash’s low latency should shift break-even point to right

## Slide 68: Why is the 10% rule wrong?
10% rule really applies to page selectivity
Index scan, uniform random layout:
[Yue et al.]
Notes: Clean up this slide
If there were exactly 1 tuple per page we would see … but for a realistic 27 tuples per page…
Focus on tuple selectivity vs page selectivity
What follows from this is that the range where index scan works
Zoom in on a point? 3% on blue?

## Slide 69: Why is the 10% rule wrong?
Implication: relation scan preferred even on flash
27 tuples/page
at 4% row sel.
expect 67% pages
10% rule really applies to page selectivity
Index scan, uniform random layout:
[Yue et al.]
Notes: If there were exactly 1 tuple per page we would see … but for a realistic 27 tuples per page…
Focus on tuple selectivity vs page selectivity
What follows from this is that the range where index scan works
Zoom in on a point? 3% on blue?

## Slide 70: Join
Join performance on disk depends on:
  Algorithm
  Relation sizes
  Projectivity
These determine
  Device access patterns
  Data read and written to device

## Slide 71: Join performance
Chart: Projectivity & Relation Sizes
| 1.9x1.9 | 3.9x3.9 | 3.9x6.8 | 6.8x6.8 | 6.8x9.7 | 9.7x9.7 | 1.9x1.9 | 3.9x3.9 | 3.9x6.8 | 6.8x6.8 | 6.8x9.7 | 9.7x9.7 | 5% projectivity (GB) |  | 25% projectivity (GB)
Disk Sort-Merge | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Disk Hybrid Hash | 1.0825 | 1.2604 | 1.179 | 1.2257 | 1.2224 | 1.0969 | 1.5013 | 0.88183 | 0.82543 | 0.83559 | 0.82119 | 0.93942
Flash Sort-Merge | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Flash Hybrid Hash | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Notes: Explain database size relative to database size
Before I hit the button talk about these results more-
With one outlier, the best join type changes with projectivity

## Slide 72: Join performance
Chart: Projectivity & Relation Sizes
| 1.9x1.9 | 3.9x3.9 | 3.9x6.8 | 6.8x6.8 | 6.8x9.7 | 9.7x9.7 | 1.9x1.9 | 3.9x3.9 | 3.9x6.8 | 6.8x6.8 | 6.8x9.7 | 9.7x9.7 | 5% projectivity (GB) |  | 25% projectivity (GB)
Disk Sort-Merge | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Disk Hybrid Hash | 1.0825 | 1.2604 | 1.179 | 1.2257 | 1.2224 | 1.0969 | 1.5013 | 0.88183 | 0.82543 | 0.83559 | 0.82119 | 0.93942
Flash Sort-Merge | 0.21527 | 0.22341 | 0.21184 | 0.21936 | 0.20322 | 0.1863 | 0.20432 | 0.12953 | 0.13226 | 0.12288 | 0.12561 | 0.12002
Flash Hybrid Hash | 0.18436 | 0.20008 | 0.19048 | 0.2152 | 0.20389 | 0.16874 | 0.20381 | 0.13431 | 0.1289 | 0.12211 | 0.12554 | 0.30442
Notes: Focus on performance different between algorithms on flash

## Slide 73: Join performance
Chart: Projectivity & Relation Sizes
| 1.9x1.9 | 3.9x3.9 | 3.9x6.8 | 6.8x6.8 | 6.8x9.7 | 9.7x9.7 | 1.9x1.9 | 3.9x3.9 | 3.9x6.8 | 6.8x6.8 | 6.8x9.7 | 9.7x9.7 | 5% projectivity (GB) |  | 25% projectivity (GB)
Disk Sort-Merge | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Disk Hybrid Hash | 1.0825 | 1.2604 | 1.179 | 1.2257 | 1.2224 | 1.0969 | 1.5013 | 0.88183 | 0.82543 | 0.83559 | 0.82119 | 0.93942
Flash Sort-Merge | 0.21527 | 0.22341 | 0.21184 | 0.21936 | 0.20322 | 0.1863 | 0.20432 | 0.12953 | 0.13226 | 0.12288 | 0.12561 | 0.12002
Flash Hybrid Hash | 0.18436 | 0.20008 | 0.19048 | 0.2152 | 0.20389 | 0.16874 | 0.20381 | 0.13431 | 0.1289 | 0.12211 | 0.12554 | 0.30442
CPU bound outlier
Flash insensitive to join type – 5.4% avg. difference w/o outlier

## Slide 74: NVRAM
Both Flash and DRAM expected to stop scaling in the next few years
  Need scalable dense replacements for both
  Numerous technologies for “Storage Class Memory” or “Universal Memory”
Resistive RAM
Phase Change
Memristor
Magnetic RAM
STT RAM
FerroElectric RAM

## Slide 75: NVRAM read performance
NVRAM read latency may be up to 5x DRAM read latency [IBM]
  Greater if not connected via main memory bus
Require DRAM/on-chip cache to accelerate reads
Traditional software-managed DRAM buffer pool or hardware-managed DRAM cache?
  Depends on capacity necessary to improve performance

## Slide 76: Read throughput
Caches likely required but even small capacity largely effective

## Slide 77: Caching
B-Trees, append-heavy, and small tables cache effectively

## Slide 78: Group Commit future work
Journal only allows so much room
Group Commit large software effort
  Useful mechanism for NVRAM persistence (not just OLTP)
Intend to include:
  Description of new data structures to efficiently track and log dirty regions
  Batch management to quickly persist batch

## Slide 79: Methodology future work
Intend to include detailed study of timing model and bandwidth reservation
More detail
Quantify accuracy and limitations

## Slide 80: Results future work
Intend to include quantitative study of:
  Persist bandwidth required for each mechanism
    Group commit is bursty, required more bandwidth
  Device lifetime due to write endurance
    Each recovery mechanism produces varying quantity of persists and distributes persists across addresses/cells differently
    Prior work imagines hardware to distribute writes to the same address across numerous cells. Consider device lifetime with hardware ware-leveling

## Slide 81: BPFS (Total Epoch Order)
Better I/O through byte-addressable, persistent memory – Condit et al.
Divide code into epochs with epoch barriers
  Persists within same epoch occur in parallel
  Persists may not reorder across barriers
  Shared memory accesses w/ at least one write imply epoch order between threads
Propose hardware (cache extensions)
No races in persist epochs (even volatile synchronization)

## Slide 82: BPFS (Total Epoch Order)
Insert(obj, size):
lock()
barrier
start = &array[counter]
memcpy(start,obj,size)
barrier
counter += size
barrier
unlock()
Buffer should persist in parallel with prev. counter
Restricts important programming patterns (batching)

## Slide 83: Partial Epoch Order (PEO)
Consider epochs from separate threads concurrent if they contain a race
  Subsequent epochs inherit order constraint
Insert(obj, size):
barrier
lock()
start = &array[counter]
memcpy(start,obj,size)
barrier
counter += size
unlock()
barrier
Similar to BPFS code
(barriers outside locks)
Buffer persists in parallel
with previous counter

## Slide 84: Partial Epoch Order (PEO)
Race with counter orders with counter’s dependencies
Adjacent insert from same thread enforces ordering
Prevents deadlock. Removes most unnecessary constraints
Too complicated to be useful?