## Slide 1: Memory Persistency
Steven Pelley, Peter M. Chen, Thomas F. Wenisch

## Slide 2: Nonvolatile memory (NVRAM)
Low latency random access, durable
NVRAM enables persistent main memory
Storage technology | Random read latency | Durable?
Disk | 10ms | 
Flash | 90µs | 
DRAM | 100ns | 
NVRAM | 50-1000ns [IBM] | 

## Slide 3: NVRAM recovery
Writes unordered!
writes
Must constrain write order for recovery
Cache eviction reorders writes to memory
Enforcing program order writes incurs 30x slowdown over instruction execution rate.
Must constrain writes for correctness, but reorder for performance

## Slide 4: Memory order
Writes to memory reorder
But loads/stores between processors and cores ordered: memory consistency

Use memory consistency to reason about NVRAM write order
?

## Slide 5: Memory persistency
Build on memory consistency, providing models to constrain NVRAM write order
Relax persistency to improve write concurrency, increasing throughput
This project: focus on models (interface), rather than implementations

## Slide 6: Outline
Define Memory Persistency
Memory persistency models
Evaluation

## Slide 7: Define Memory Persistency
Memory consistency:
Constrain order of loads and Stores Between processors
Memory persistency:
Imagine failure as recovery observer
Atomically loads all of memory
If two stores are ordered, then the associated persists also ordered

## Slide 8: Memory Persistency Design Space
Persistency
Consistency
Sequential consistency (SC), persistent state must match volatile state
Loads, stores, and persists may all reorder. Complex, but minimizes delays for both persists and concurrency control
SC, but persistent state de-coupled from volatile states. Persists may reorder
Relaxed consistency, persistent state still matches some volatile state
Persist order determined by new persist barriers
Persist order determined by consistency model
strict
relaxed

## Slide 9: Outline
Define Memory Persistency
Persistency models
Evaluation

## Slide 10: Persistent Queue
Useful as log/journal in file systems and db
Features:
  Serialize inserts
  Recovered queue disallows or detects holes
Goal: maximize volatile performance (instruction execution rate) and improve persist concurrency for inserts
Implementation: based on circular buffer
  Data segment, head marks next location to insert

## Slide 11: Queue Designs
Copy-while-locked (CWL)
  Single lock protects insert operation
Two-Lock Concurrent
  Different locks to reserve and update head
  Lesson: thread concurrency creates persist concurrency even for strict persistency
Queue-holes
  Detect holes. Single lock but concurrent copies
Focus on CWL (see dissertation for others)

## Slide 12: Copy-While-Locked Queue
Insert(entry, length):
lock(queue_lock)
data[head] = length
data[head+sizeof(length)] = entry
head += length + sizeof(length)
unlock(queue_lock)
Data
Head
Persistency model must enforce persist orderings
Persist Ordering Constraints

## Slide 13: Persistency assumptions and goals
Assume persist buffering
  Thread state proceeds ahead of persists
  But persists still occur in proper order
  Persist order critical path limits performance
Assume persist coalescing
  Persists to the same address may coalesce (persist only last value) if no ordering constraints violated
Goal: create models to minimize critical path

## Slide 14: New persistency models
All models use SC as consistency model
  Easier to reason about (removes relaxed consistency/relaxed persistency weirdness)
  Easier to evaluate (memory tracing observes SC)
Successively relax persistency to improve persist concurrency/reduce critical path

## Slide 15: Strict persistency
Any volatile memory state that might be observed by the recovery observer processor under SC is an allowable persistent state
Equivalent: two stores guaranteed to be ordered w.r.t. recovery observer implies ordered persists
Persist sync allows ordering persists with visible side effects (syscall)

## Slide 16: Strict persistency queue
Persist order determined by program order
Insert(entry, length):
lock(queue_lock)
data[head] = length
data[head+sizeof(length)] = entry
head += length + sizeof(length)
unlock(queue_lock)
Data persists before head without extra work
Serializes persists of large entries to program order
Lock serializes persists between all insert calls

## Slide 17: Strict persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2
Minimal dependences shown. Persists to head likely to coalesce

## Slide 18: Strict persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2
Guarantees correct recovery, but over-constraints persists

## Slide 19: Strict persistency implementations
Delay execution at each persist
Serialize persists when reserving memory bus
Queue persists from each thread, detecting access races (including synchronization races) that introduce order across threads
Combine HTM and hardware durable transactions
  Persistent bulkSC?

## Slide 20: Epoch persistency
Motivation: persisting large objects with SC introduces program-order constraints
Instead, use persist barrier to divide execution into persist epochs
Persists within each epoch are concurrent
Determining persist order between threads can get tricky

## Slide 21: Persist epoch races (PER)
Under what circumstances are persists between threads ordered?
Persist epoch race: 2+ threads contain epochs that race (including synch. races) and at least one epoch persists
Thread 1
Persist A
Persist B
Barrier
Thread 2
Read B
Barrier
Persist C
Can C persist before A?
Can C persist before B?
Epochs aren’t serializable!

## Slide 22: Epoch persistency queue, 1st attempt
Insert(entry, length):
barrier()
lock(queue_lock)
barrier()
data[head] = length
data[head+sizeof(length)] = entry
barrier()
head += length + sizeof(length)
barrier()
unlock(queue_lock)
barrier()
Surround lock/unlock with barriers to prevent persist epoch races
Barrier ensures head does
not persist before data

## Slide 23: Race-free epoch persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2

## Slide 24: Race-free epoch persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2

## Slide 25: Race-free epoch persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2
Entries persist in parallel, but inserts still serialized

## Slide 26: Defining PER behavior
Persist A ordered before persist B if:
  Observe A persisted prior to barrier preceding B
  Or A and B are to the same address
Thread 1:
Persist A
Barrier
Persist B
Store V
Thread 2:
Read V
Persist B’
Persist C
Barrier
Persist D
Ordering constraints:
A before B
B’ before D
C before D
B before B’ (cache coherence)
A before D (through V)
No constraint:
A and B’
A and C
B and C
B and D
B’ and C

## Slide 27: Epoch persistency queue, 2nd attempt
Insert(entry, length):
barrier()
lock(queue_lock)
barrier()
data[head] = length
data[head+sizeof(length)] = entry
barrier()
head += length + sizeof(length)
barrier()
unlock(queue_lock)
barrier()
Allow persist epoch races
head persists ordered by cache coherence

## Slide 28: Epoch persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2

## Slide 29: Epoch persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2

## Slide 30: Epoch persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2
Entries on different threads persist in parallel

## Slide 31: Epoch persistency implementation
Similar to BPFS (see paper/dissertation)
Queue persists from each thread, record persist barriers, only enforce order at barriers
Persistent BulkSC (transactions)
  Use persist barrier knowledge to optimize persistent transactions and intelligently place transaction boundaries

## Slide 32: Strand persistency
Motivation: epochs only allow adjacent persists on same thread or persists in racing epochs to be labeled concurrent
Divide execution into strands
  NewStrand begins a strand
  Strands execute in order on a thread, but from perspective of persistency are independent.
  Equiv: a new strand clears persist dependences
  Races/conflicts introduce order between strands
Epoch pers. orders persists within strands

## Slide 33: Strand examples
Strands allow precise persist constraint labeling
A
B
C
...
Epoch
A
Barrier
B
C
A
B
Barrier
C
Extra constraint introduced between B and C
or
Strand
NewStrand
A
Barrier
C
NewStrand
B
...

## Slide 34: Perfect constraint labeling
Strands can perfectly label constraints
For each persist:
  New strand
  Read all addresses persist depends on
  Barrier
  Persist
Minimal persist dependences (additional instructions required)

## Slide 35: Strand persistency queue
Insert(entry, length):
lock(queue_lock)
new_strand()
data[head] = length
data[head+sizeof(length)] = entry
barrier()
head += length + sizeof(length)
unlock(queue_lock)
Removes unnecessary dependences between insert operations

## Slide 36: Strand persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2

## Slide 37: Strand persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2

## Slide 38: Strand persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2
Back to minimal dependences

## Slide 39: Outline
Define Memory Persistency
Persistency models
Evaluation

## Slide 40: Methodology
Produce SC memory trace of queue from PIN
Annotate barriers, persistent malloc, etc.
Simulate persist performance assuming persists are only cause of delay
  No additional delays (infinite bandwidth, banks)
Measure persist critical path
  Dependences tracked at 8-byte granularity
  Persists to same address coalesce if no constraints violated (assume atomic 8-byte persists)
  Constraints determined by persistency model

## Slide 41: Relaxed persistency
Relaxed persistency removes constraints and regains throughput

## Slide 42: Persist latency
Relaxed persistency tolerates greater persist latency

## Slide 43: Conclusion
Recovery requires constrained persist order
Over-constraining persists limits throughput
This tradeoff resembles memory consistency
Memory persistency builds on consistency to enforce persist order where necessary and increase persist concurrency elsewhere
Memory persistency achieves instruction execution rate with recovery correctness

## Slide 44: [dependence template]
Data
Head
Data
Head
Thread 1
Thread 2