## Slide 1: High Performance Transaction Processing for NVRAM
Steven Pelley, Thomas F. Wenisch
University of Michigan

## Slide 2: Nonvolatile memory (NVRAM)
New NVRAMs provide fast durable storage (phase change, memristor, STT-RAM)
NVRAM enables persistent main memory
Storage technology | Random read latency | Durable?
Disk | 10ms | 
Flash | 90µs | 
DRAM | 100ns | 
NVRAM | 50-1000ns [IBM] | 

## Slide 3: Recoverable systems
Must protect data against server failure
  E.g., file systems and databases
  Typically rely on disk, flash for persistent storage
NVRAM accelerates persistent storage access
  Byte-addressable (native memory instructions) further decrease execution overheads
Create recoverable, high performance data structures (main-memory/DRAM speed)
NVRAM requires new recovery mechanisms

## Slide 4: Optimizing NVRAM
Case study of transaction processing [VLDB]
  NVRAM as a disk replacement (ARIES/WAL)
  Fast NVRAM imposes frequent persist ordering
  New software design to avoid ordering delays
Future work: explore desirable optimizations and semantics for NVRAM memory systems

## Slide 5: NVRAM as a disk replacement
Write Ahead Logging (WAL) via ARIES
Complexity necessary for slow disk now excessive overhead
Transaction thread
Update
Log flusher
Log buffer
Page flusher
Buffer cache
Defer persists
Persist from specialized threads
Serialize log records

## Slide 6: Alternative: order persists immediately
Persist barriers [BPFS: SOSP ‘09]
  Persists following barrier instruction may not complete before persists prior to barrier
  Persists that are not separated by barrier instruction are concurrent
Barriers delay execution
  Frequency of barriers and exposed barrier latency determine resulting performance

## Slide 7: NVRAM in-place updates
Simple, removes software overhead, but frequent persist ordering
Transaction thread
Update
Transaction/update logs
Heap
Persist immediately
Remove centralized log
Barriers necessary at each update

## Slide 8: NVRAM Group Commit
Time
Volatile update
buffer
NVRAM
log
NVRAM
store
Persist log
Persist heap
Transactions quiesce at end of batch
Batch’s updates persist to batch log, then in place
Persist barriers

## Slide 9: NVRAM Group Commit
Time
Persist log
Persist heap
Constant number of persist barriers per batch
No centralized logging
Throughput high so long as batch quiesce/persist short
Several other tradeoffs (e.g., increased transaction latency)
Persist barriers

## Slide 10: Modeling unavailable devices
Run database on real hardware
  Log and db heap on RAMDisk (or just in DRAM)
  Introduce precise delays (20ns precision using x86 RDTSCP) to model persist barrier latency
Build recovery mechanisms in software
  Shore-MT: research platform for high performance transaction processing
  Rely on dirty bit fields to track buffer pool writes during transaction, page latch, or batch

## Slide 11: Recovery management performance
Group commit recovers throughput when barrier latency exposed
TPCB benchmark
High performance barriers and memory system ideal
Disk replacement insensitive to latency, but slow

## Slide 12: In the VLDB paper…
Implementation and methodology details
Persist bandwidth modeling
Group commit trade-offs and transaction latency analysis
Read-cache performance based on memory trace analysis

## Slide 13: Future work: NVRAM optimizations
Asynchronous persists
  Allow execution to proceed ahead of persists
  Hides persist and persist barrier latency
  Persist ordering critical path limits persist rate
Persist coalescing
  Omit persists if ordering constraints not violated
  Acts as bandwidth filter (like write-back cache)
  Reduces persist ordering critical path
Need mechanisms to precisely label persist ordering constraints
[upcoming ISCA: Memory Persistency]

## Slide 14: Conclusion
Disk-based software carries baggage
Frequent persist synchronization also slow
New software and memory systems improve performance and simplify software design
References
  Website: http://web.eecs.umich.edu/~spelley
  Steven Pelley, Thomas F. Wenisch, Brian T. Gold, Bill Bridge: Storage Management in the NVRAM Era. PVLDB 7(2): 121-132 (2013)
  [BPFS] Jeremy Condit, Edmund B. Nightingale, Christopher Frost, Engin Ipek, Benjamin Lee, Doug Burger, and Derrick Coetzee. 2009. Better I/O through byte-addressable, persistent memory. In Proceedings of the ACM SIGOPS 22nd symposium on Operating systems principles (SOSP '09)

## Slide 15: Backup slides

## Slide 16: Disk replacement performance
As disk replacement NVRAM enables near-instant recovery
Disk-management overheads impose bottleneck
~ 30 15krpm disks
or 3 Flash SSDs
[device IOPS rates: Symantec]
TPCB benchmark
Place log and store on RAMDisk
Artificially limit write IOPS
+50%

## Slide 17: Memory persistency [upcoming ISCA]
Writes to memory reorder due to write-back caches
But loads/stores between processors and cores ordered: memory consistency

Extend memory consistency to reason about NVRAM write order: Memory Persistency
?