## Slide 1: Database and System Design for Emerging Storage Technologies
Steven Pelley
Committee:
Thomas F. Wenisch (Chair)
Michael J. Caffarella
Peter M. Chen
Zhengya Zhang

## Slide 2: Nonvolatile memory (NVRAM)
DRAM and flash will stop scaling
New NVRAMs provide fast, scalable storage (phase change, memristor, STT-RAM)
NVRAM enables persistent main memory
Storage technology | Random read latency | Durable?
Disk | 10ms | 
Flash | 90µs | 
DRAM | 100ns | 
NVRAM | 50-1000ns [IBM] | 

## Slide 3: Recoverable systems
Must protect data through failure
  E.g., file systems and databases
  Typically rely on disk, flash for persistent storage
NVRAM provides faster persistent storage
  Redesign software assuming fast access
  Byte-addressable (native memory instructions) further decrease execution overheads
NVRAM requires new recovery mechanisms

## Slide 4: Protecting data through failure
Must constrain order of writes (persists)
  Disk: stall next request until previous completes
However, memory allows writes to reorder
  Cache eviction order ≠ store order
NVRAM requires persist barriers
  Semantics, implementation, and performance implications uncertain
  At worst stall until persist completes to memory
Despite fast NVRAM accesses, persist barriers limit performance

## Slide 5: Example: transaction processing (VLDB)
NVRAM as disk replacement (write ahead logging)
Complexity necessary for slow disk now excessive overhead
Transaction thread
Update
Log flusher
Log buffer
Page flusher
Buffer cache
Defer persists
Persist from specialized threads
Serialize log records

## Slide 6: Example: transaction processing (VLDB)
NVRAM In-place updates
Simple, remove software overhead, but frequent persist barriers
Transaction thread
Update
Transaction log
Heap
Persist immediately
Barriers order persists to log and heap

## Slide 7: Example: transaction processing (VLDB)
Transaction throughput
≤ 100ns
~1-10µs
≥100µs
NVRAM Disk
In-place updates provides max throughput only at low latency
In-place Updates
?
Average exposed persist barrier latency

## Slide 8: Example: transaction processing (VLDB)
Undo log
Updates
Constant number of persist barriers per batch
Amortize persist barrier cost over many transactions
But several limitations (transaction latency, long transactions)
Transactions quiesce at end of batch
Transaction updates write atomically using batch log
NVRAM group commit
persist barriers

## Slide 9: Example: transaction processing (VLDB)
Transaction throughput
≤ 100ns
~1-10µs
≥100µs
NVRAM disk
Group commit fast, but Ideally hide persist latency entirely
In-place updates
Average exposed persist barrier latency
Group commit

## Slide 10: Practical persist barriers
How do we minimize barrier stalls?
How are persists ordered across threads?
Why use persist barriers at all?
  Enforce program order of persists
Explore fundamental primitives for persist synchronization

## Slide 11: Memory ordering
Writes to memory reorder
But loads/stores between processors and cores ordered: memory consistency

Extend memory consistency to reason about NVRAM write order: Memory Persistency
?

## Slide 12: Thesis
Using Flash memory for database analytics
  [ADMS 2011]
Using NVRAM to accelerate transactions
  [VLDB 2014]
Memory persistency
  Extend consistency to reason about persist order
  Enforcing program-order persists limits throughput to 1/30th instruction execution rate
  Relaxed persistency models regain performance

## Slide 13: Outline
Motivate memory persistency
Memory consistency review
Define memory persistency
Persistent queue benchmark
Memory persistency models
Methodology
Evaluation

## Slide 14: Outline
Motivate memory persistency
Memory consistency review
Define memory persistency
Persistent queue benchmark
Memory persistency models
Methodology
Evaluation

## Slide 15: Outline
Motivate memory persistency
Memory consistency review
Define memory persistency
Persistent queue benchmark
Memory persistency models
Methodology
Evaluation

## Slide 16: Memory consistency primer
Motivation: reorder instructions while providing intended shared memory behavior
Barrier
Thread 2:
If (Flag == 1) {
localBuffer[0] ← Buffer[0]
localBuffer[8] ← Buffer[8]
…
}
In isolation may reorder, but when sharing must constrain
Thread 1:
Buffer[0] ← 1
Buffer[8] ← 1
…
Flag ← 1
Barrier

## Slide 17: Memory consistency models
Consistency spectrum
Guarantees for reasoning about reordering
Sequential Consistency (SC): no reordering, memory appears as a switch to processors
Relaxed Memory Order (RMO): any reordering possible, must use barriers
Model separate from implementation

## Slide 18: Outline
Motivate memory persistency
Memory consistency review
Define memory persistency
Persistent queue benchmark
Memory persistency models
Methodology
Evaluation

## Slide 19: Recovery observer
Memory consistency:
Constrain order of loads and stores between processors
Memory persistency:
Imagine failure as recovery observer
Atomically copies to NVRAM at failure, adhering to consistency model
Treats failure as a processor
Enforcing NVRAM write order equivalent to enforcing store order

## Slide 20: Strict persistency
Couples consistency and persistency
  1:1 mapping between observable volatile and persistent states
Two stores that may only be observed in some order imply ordered persists
  The store and the persist are the same event
Consistency model and barriers constrain persist order and thread synchronization
Implementation free to optimize

## Slide 21: Buffered persistency
Thread execution (volatile state) proceeds ahead of persistent state
  Persist and store are separate events!
Problem: side effects violate model
Persist sync forces durable state to “catch up”
…
Persist to object A
PersistSync
Syscall() // network
…
May observe syscall but after recovery fail to see persist to A
PersistSync constrains order

## Slide 22: Relaxed persistency
Decouple thread synchronization and persists
  Persist order may deviate from store order
New persist barriers order persists
Allows thread to observe persist values without introducing order dependence
Later I’ll introduce relaxed persistency models assuming SC as underlying consistency model

## Slide 23: Relaxed persistency example
Lock()
Persist 0x100
Persist 0x108
…
Persist Flag=1
Unlock()
Lock/Mutex provides thread synchronization, but no need to additionally enforce persist order at this point
Flag must not persist before data, but as the lock protects against races an additional memory barrier is unnecessary
Memory barrier
Persist barrier
Memory barrier
Precise, independent control over consistency and persistency
Stores reorder around persist barriers, persists reorder around store barriers.
Simultaneously relaxed consistency and persistency gets complicated.

## Slide 24: Outline
Motivate memory persistency
Memory consistency review
Define memory persistency
Persistent queue benchmark
Memory persistency models
Methodology
Evaluation

## Slide 25: Persistent queue
Useful as log/journal in file systems and db
Goal: maximize volatile performance (instruction execution rate) and improve persist concurrency for inserts
Implementation: based on circular buffer
  head marks next location to insert
Examples here are simplified
Dissertation: two additional queue designs

## Slide 26: Queue operation
Insert(entry, length):
lock(queue_lock)
data[head] = length // prepend with length
data[head+sizeof(length)] = entry
head += length + sizeof(length)
unlock(queue_lock)
Data
Head
Persistency model must enforce persist orderings
Persist Ordering Constraints

## Slide 27: Outline
Motivate memory persistency
Memory consistency review
Define memory persistency
Persistent queue benchmark
Memory persistency models
Methodology
Evaluation

## Slide 28: Persistency assumptions and goals
Assume all persists occur in-place (no logging)
Assume persist buffering
  Persist critical path limits persist rate
Assume limited atomic persists and coalescing
  E.g., 8-byte atomic persists
  Persists to the same address may coalesce (persist only last value) if no ordering constraints violated
Use SC as underlying consistency model
Goal: create models to minimize persist critical path

## Slide 29: Model 1: strict persistency
A volatile memory state observed by the recovery observer processor under SC is an allowable persistent state
Equivalent: if two stores ordered w.r.t. recovery observer, persists also ordered
  Same thread: program order
  Different threads: synchronization and conflicts
  If not ordered: concurrent!

## Slide 30: Strict persistency queue
Persist order determined by program order
Insert(entry, length):
lock(queue_lock)
data[head] = length
data[head+sizeof(length)] = entry
head += length + sizeof(length)
unlock(queue_lock)
Lock serializes persists between threads
Large queue entries persist in program order
No code annotation necessary!

## Slide 31: Queue required dependences
Data
Head
Data
Head
Thread 1
Thread 2

## Slide 32: Strict persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2
Guarantees correct recovery, but over-constrains persists

## Slide 33: Model 2: epoch persistency
Motivation: strict persistency introduces program-order constraints.
Instead, use persist barrier to enforce an ordering constraint between persists
  Execution divided into persist epochs
Data sharing continues to observe SC
Persist order resembles RMO, persist barrier acts as a full memory barrier

## Slide 34: Epoch persistency queue
Insert(entry, length):
barrier()
lock(queue_lock)
barrier()
data[head] = length
data[head+sizeof(length)] = entry
barrier()
head += length + sizeof(length)
barrier()
unlock(queue_lock)
barrier()
Surround lock/unlock with barriers. Persists ordered by lock accesses
Barrier ensures head does
not persist before data, but data persists concurrently

## Slide 35: Epoch persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2

## Slide 36: Epoch persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2

## Slide 37: Epoch persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2
Entries persist in parallel, but inserts still serialized

## Slide 38: Epoch persistency ordering
Separate volatile memory order and persistent memory order
  Volatile order fulfills SC
  Persistent order contains subset of constraints
Rule 1: memory operations from same thread separated by persist barrier are ordered
Rule 2: conflicting operations (same address, at least 1 store/persist) ordered
Rule 3: 8-byte persists atomic with respect to recovery observer

## Slide 39: Persist ordering example
Rule 1: A before {B, C}; {C’, D} before E; E’ before F
Rule 2: C before C’; E before E’
Trans: A before {C’, E, E’, F}; C before {E, E’, F}…
B concurrent with shown accesses on T2, T3
  Even if value of C depends on B
D concurrent with shown accesses on T1
Dependences propagate through volatile address space
Thread 1: A | B C
Thread 2: C’ D | E
Thread 3: E’ | F
conflict

## Slide 40: Epoch persistency queue, 2nd attempt
Insert(entry, length):
barrier()
lock(queue_lock)
barrier()
data[head] = length
data[head+sizeof(length)] = entry
barrier()
head += length + sizeof(length)
barrier()
unlock(queue_lock)
barrier()
Allow persist epoch races
head persists from different inserts ordered due to conflicts

## Slide 41: Epoch persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2

## Slide 42: Epoch persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2

## Slide 43: Epoch persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2
Entries on different threads persist in parallel

## Slide 44: Model 3: strand persistency
Motivation: epochs allow limited concurrency
Divide execution into strands
  NewStrand begins a strand
  Strands execute in order on threads, but NewStrand clears persist dependences
Epoch pers. orders persists within strands
Change Epoch persistency rule 1:
  Memory operations from same strand separated by persist barrier are ordered
New accesses accumulate dependences

## Slide 45: Strand example
Strands allow precise persist constraint labeling
A
B
C
...
Epoch
A
Barrier
B
C
A
B
Barrier
C
B must be ordered with A and/or C
or
Strand
NewStrand
A
Barrier
C
NewStrand
B
...

## Slide 46: Perfect constraint labeling
For each persist:
  New strand
  Read all addresses persist depends on
  Barrier
  Persist
Creates DAG of dependences. Edge from each read to persist
Minimal persist dependences (introduces additional instructions)

## Slide 47: Strand persistency queue
Insert(entry, length):
lock(queue_lock)
new_strand()
data[head] = length
data[head+sizeof(length)] = entry
barrier()
head += length + sizeof(length)
unlock(queue_lock)
Removes unnecessary dependences between inserts

## Slide 48: Strand persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2

## Slide 49: Strand persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2

## Slide 50: Strand persistency dependences
Data
Head
Data
Head
Thread 1
Thread 2
Back to minimal dependences

## Slide 51: Outline
Motivate memory persistency
Memory consistency review
Define memory persistency
Persistent queue benchmark
Memory persistency models
Methodology
Evaluation

## Slide 52: Methodology
Assume buffered NVRAM with infinite banks (no conflicts ever occur). All persists occur in place (no logging but persists may coalesce)
  Persists drain faster than instruction execution rate; instructions limit performance
  Persists drain slower than instruction execution rate; persist rate limits performance
Determine throughput from slower of two
Real systems likely delay elsewhere to persist

## Slide 53: Methodology
Measure execution rate on real server
  2.4 GHz Xeon E5645
  Use 1 and 8 threads to test concurrency
  Pad to 64 bytes to remove false sharing
  Repeatedly insert 100-byte entries as quickly as possible, reporting insert rate

## Slide 54: Methodology
Measure persist rate via memory traces
  Produce SC memory trace from PIN
  Annotate barriers, persistent malloc, etc.
Persist critical path from simulation
  Track persist dependences at variable granularity
  Persists coalesce assuming variable atomic persist
  (both 8 bytes by default)
  Observe persist timing and dependences from persistency model

## Slide 55: Outline
Motivate memory persistency
Memory consistency review
Define memory persistency
Persistent queue benchmark
Memory persistency models
Methodology
Evaluation

## Slide 56: Relaxed persistency
Relaxed persistency removes constraints and regains throughput
Line indicates instruction execution rate
Assumes 500ns persists
30x
Other queues

## Slide 57: Persist latency
Relaxed persistency tolerates greater persist latency
17ns
119ns
6.2µs
1 Thread
(8 Threads)

## Slide 58: Persist coalescing
Larger atomic persists improve concurrency for strict models

## Slide 59: Persistent false sharing
Coarse dependence tracking reintroduces constraints

## Slide 60: What’s next?
Design hardware
  What relaxations give best performance?
  How do we track dependences and persist values (in cache, in queues?)
  How do we correctly coalesce?
New workloads, data structures, services

## Slide 61: Conclusion
Must order persists, but over-constraining hurts performance (resembles consistency)
Memory persistency builds on consistency to enforce persist order
Persistency may be relaxed, de-coupling store and persist order constraints
Relaxed persistency enables instruction execution rate with recovery correctness

## Slide 62: Thank You!
Thanks to my family, friends, Tom, committee, collaborators, and all of you
Questions?

## Slide 63: Backup Slides
Persistency definition
  Defining order of persists to same address
Queue
  Circular buffer
  Other queue designs
Results
  Coalescing
  Relaxed persistency, all queues
  Effect of latency on CWL, 8 threads
Alternative interfaces
  Disk/block
    Moneta
  Transactions
    Various [Mnemosyne, RIO Vista, STM]
    Kiln-decouple thread synchronization from persistency control
  Barriers
    BPFS

## Slide 64: Persists to same address
Strict persistency relies on consistency model to define order or persists to same address
  Often relies on cache coherence guarantees
Relaxed consistency/relaxed persistency allows:
  Store visibility to reorder across persist barrier
  Persists to reorder across store barrier
May violate cache coherence persist ordering

## Slide 65: Persists to same address
Thread 1’s stores reorder around the barrier
Persist ordering dependences shown for barriers and cache coherence order
Dependence cycle cannot be enforced
Thread 1:
Persist A
Barrier
Persist B
Thread 2:
Persist B
Barrier
Persist A

## Slide 66: Persists to same address
Resolve by:
  Relying on strict persistency
  Preventing stores from reordering around persist barriers
  Defining additional synchronization to prevent such situations
    Interaction between consistency barriers and persist barriers
Back
Backup slides

## Slide 67: Coalescing
Any two persists may coalesce if:
  Hardware allows them to persist atomically
  No happens-before constraints are violated
Given a DAG of persist constraints, coalescing:
  Combines the two persists into a single node
  Persist value taken from last persist
  Node takes union of edges into and out of node
  Edges entirely inside the node go away
  Coalescing legal if no cycles introduced

## Slide 68: Coalescing example
A
B
A’
B
A’
Cycle!
C
D
C’
A
B
E
A
B
C’
D
E

Back -- Backup slides

## Slide 69: All queues, 1 thread
Varied volatile performance. Require strand persistency

## Slide 70: All queues, 8 threads
Multi-threading improves persist concurrency. Epoch sufficient
Back -- Backup slides

## Slide 71: Latency, CWL 8 threads
Epoch persistency likely sufficient
28ns
1.6µs
10.5µs
PER-free: 202ns (not shown)
Back -- Backup slides

## Slide 72: BPFS
“Better IO Through Byte-Addressable, Persistent Memory”
Cache implementation of barriers and epochs
  Stalls to persist at thread conflicts
  Flush cache for persist sync
Different from epoch persistency
  Programmer must provide isolated epochs (including false sharing, otherwise deadlock)
  No dependences through volatile memory
  Loads may bypass store in persist order (persist barrier is 3/4 RMO barrier; similar to TSO)
Back Backup slides

## Slide 73: [dependence template]
Data
Head
Data
Head
Thread 1
Thread 2

## Slide 74: PER persist ordering
Thread 1: A | B C
Thread 2: C’ D | E
A before E (race and barriers)
C before C’ (cache coherence)
A before C’ (transitivity)
C before E (transitivity)
PersistPersist race good candidate for coalescing
PersistPersist
Thread 1: A | B C
Thread 2: load C’ D | E
C before E
A before E (transitivity; A before C)
PersistLoad
Thread 1: A | B load C
Thread 2: C’ D | E
load C before E
A before E (transitivity)
A before C’
LoadPersist
Resembles RMO with full barriers
Thread 1: A | B
Thread 2: B’ | C
Thread 3: C’ | D
A before D (race and barriers)
Red barrier required
B, C volatile

## Slide 75: Memory Persistency
Steven Pelley, Peter M. Chen, Thomas F. Wenisch

## Slide 76: NVRAM recovery
Writes unordered!
writes
Must constrain write order for recovery
Cache eviction reorders writes to memory
Enforcing program order writes incurs 30x slowdown over instruction execution rate.
Must constrain writes for correctness, but reorder for performance

## Slide 77: Example: transaction processing (VLDB)
As disk replacement NVRAM enables near-instant recovery
Disk-management overheads impose bottleneck
~ 30 15krpm disks
or 3 Flash SSDs
[device IOPS rates: Symantec]
TPCB benchmark

## Slide 78: Recovery management performance
Group commit helps, but high performance barriers ideal

## Slide 79: Memory Persistency Design Space
Persistency
Consistency
Sequential consistency (SC), persistent state must match volatile state
Loads, stores, and persists may all reorder. Minimizes delays for persists and thread synchronization
SC, but persistent state de-coupled from volatile states. Persists may reorder
Relaxed consistency, persistent state matches volatile state
Persist order determined by new persist barriers
Persist order determined by consistency model
strict
relaxed

## Slide 80: Strict persistency implementations
Delay execution at each persist
Serialize persists when reserving memory bus
Queue persists from each thread, detecting access races (including synchronization races) that introduce order across threads
Combine HTM and hardware durable transactions
  Persistent bulkSC?

## Slide 81: Epoch persistency implementation
Similar to BPFS (see paper/dissertation)
Queue persists from each thread, record persist barriers, only enforce order at barriers
Persistent BulkSC (transactions)
  Use persist barrier knowledge to optimize persistent transactions and intelligently place transaction boundaries

## Slide 82: Load-store conflicts
Imagine:
  C is a load
  C’ is a store/persist
  Still a conflict!
Difficult to implement, typically load-store conflict does not imply order with previous stores/persists (e.g., TSO)
Thread 1: A | B C
Thread 2: C’ D | E
Thread 3: E’ | F
conflict

## Slide 83: Persist epoch races (PER)
Under what circumstances are persists between threads ordered?
Persist epoch race: 2+ threads contain epochs that race (including sync. races) and at least two epochs persist
Thread 1
P. barrier
Persist A
Persist B
P. barrier
Thread 2
P. barrier
Read B
Persist A’
P. barrier
Can A’ persist before A?
Can A’ persist before B?
Epochs aren’t serializable!